## Slide 1: Camera Installation Guide w/ SmartNav 2.0
Parts required to order from PACCAR Parts
1x PP207020 Adaptor Harness. This allows up to 4 cameras to be connected

## Slide 2: Adaptor Harness PP207020

## Slide 3: Two Camera Vendors via PACCAR Parts
Pana-Pacific
  Left, Right, Forward, and Back-up Camera available
  Installation Instructions – See following slides
Velvac Camera Kits
  Left, Right, Forward, Camera available
  Installation Instructions – See following slides

## Slide 4: Pana-Pacific Cameras/Jumpers Through PACCAR Parts
Cameras
Available Camera kits. Kits include a camera and extension harness.
PP807032 – Front Camera with 16 ft cable
PP804395 – Rear Camera with 70 ft cable
PP804396 – Right Side Camera with 16 ft cable
PP804397 – Left Side Camera with 16 ft cable
Jumpers
Extension cables are available if a longer length is required:
RRC-10: 10 ft extension
RRC-1: 16 ft extension
RRC-35: 35 ft extension
RRC-70: 70 ft extension

## Slide 5: Velvac Cameras/Jumpers Through PACCAR Parts

## Slide 6: Velvac Cameras/Jumpers Through PACCAR Parts

## Slide 7: Velvac Cameras/Jumpers Through PACCAR Parts

## Slide 8: Camera Installation Block Diagram

## Slide 9
PP207020 Adaptor Harness Plugs into Back of the Head Unit.
The existing harness plug connects to the PP2010220 Adaptor Harness.
Adaptor Harness
PP207020
4x Camera Inputs
Display DEA 600 connection
Existing Harness connection
Radio Head Unit DEA 610 connection

## Slide 10
Adaptor Harness PP207020
Connection Display DEA 600
Display DEA 600 connection
Display DEA 600 connection

## Slide 11
P92-8917
Radio Head Unit DEA 610 connection
Adaptor Harness PP207020
Connection Radio Head Unit DEA 610

## Slide 12: Camera Connections 4x Camera Inputs

## Slide 13: Camera Configuration Options
Camera
  Video Input 1 – Reverse (Back-up) Camera
  Video Input 2 – Forward Facing Camera
  Video Input 3 – Right Turn Camera
  Video Input 4 – Left Turn Camera
Cameras can be configured to be selected manually or Automatically (Via J1939 CAN Messages)
In Manual mode the user select the camera view
In Auto mode the camera view is selected automatically depending on the truck state
  Left turn signal active
  Right turn signal active
  Reverse active
  Front default
  Note the user may manually select the camera view when left, right turn signal or reverse is not active

## Slide 14: Camera Views
Select camera views in “Home” screen to access the available camera views

## Slide 15: Camera Display Activation DEA 600
To configure the cameras within the DEA 600 Display
Enter camera views application select the desired camera view and activate “ON”

## Slide 16: Camera Display Activation DEA 600
To configure the cameras within the DEA 600 Display
Enter the Advanced Menu and follow the steps:
  Simultaneously select the following hard keys Home & Brightness . Hold for greater than 8 seconds. The display will enter the “Advanced Menu”
  Scroll down to page 2

## Slide 17: Camera Display Activation DEA 600
  Page 2 Select Camera Required

## Slide 18: Camera Display Activation DEA 600
  Scroll up to page 1
  Select “SAVE”
  Pop Up Save Configuration appears “OK” or “Cancel” Select “OK”
  System Reboots
  Cameras are now active and manually selectable within the camera view menu
  Completed
  To set Cameras to Auto follow the steps above and continue the procedure using ESA. The ESA process is described in the next slides

## Slide 19: Camera Views
To activate a camera view, select the Forward, Right, Left or Reverse soft key indicated on the display truck graphic

## Slide 20: Example Camera View (Right)

## Slide 21: Automatic Mode
Automatic Camera Mode by Model
Camera activation DEA 600
  Cameras must be set to on within the DEA 600
Peterbilt Auto Camera Availability |  | 
Model | Auto Camera | 
325 | NO | 
330 | NO | 
337 | NO | 
348 | NO | 
382 | NO | 
320 | NO | 
365 | YES | 
367 | YES | 
389 | YES | 
587 | NO | 
567 | YES | 
579 | YES | 
Kenworth Auto Camera Availability |  |  | 
Model | LH Camera | RH Camera | Reverse Camera
T270 | YES | YES | NO
T370 | YES | YES | NO
T440 | YES | YES | ???
T460 | YES | YES | ???
T470 | YES | YES | ???
C500 | YES | YES | YES
T660 | YES | YES | YES
T680 | YES | YES | YES
T800 | YES | YES | YES
T880 | YES | YES | YES
W900 | YES | YES | YES

## Slide 22: ESA Procedure for Setting Automatic Camera Mode
Program area of ESA (use the program button at top),
  Look under the network interface tab.
    Enable Router should be set to “Enable”
    Transmit CECU LC Message should be set to “Gateway or Route to VCAN”
    NAMUX 3

## Slide 23: ESA Procedure for Setting Automatic Camera Mode
Program area of ESA (use the program button at top),
  Look under the network interface tab.
    Enable Router should be set to “Enable”
    Transmit CECU LC Message should be set to “Gateway or Route to VCAN”
    NAMUX 4

## Slide 24: ESA Procedure for Setting Automatic Camera Mode
Program area of ESA (use the program button at top),
  Look under the network interface tab.
    Enable Router should be set to “Enable”
    Transmit CECU LC Message should be set to “Gateway or Route to VCAN”
Once these are set, should see the lighting information on the bus.
  Provides info SmartNav needs for the Automatic mode in the camera screen.
Note: Cameras will only work in automatic mode if the SmartNav is put in camera mode.
  If in GPS mode or something else - camera view won't automatically pop up

## Slide 25: J1939 CAN Messages
CAN Messages are used to activate camera views:
  SPN 2367, PGN 65089 Left Turn Signal
  SPN 2369, PGN 65089 Right Turn Signal
  SPN 2391, PGN 65089 Backup Light
Note: no message to activate the forward facing camera. The only way for a user to access it is to go the camera screen under the truck menu where it is the default camera view.