## Slide 2: MK1.4 +AC Generator
November 21st, 2021

## Slide 3: Outline
Problem Statement
Mitigation Plans
1.4+AC Generator next steps

## Slide 4: Problem
Chip shortages constrain the supply of Bel inverters. The 1.4 requires (2) Bel Inverters (Arena P/N 10000663, Mfg P/N BCV200-350-8S577).
Delivery of production quantities of inverters were pushed back from Jan 2022 to June 2022
There is line of sight on (70) MK’s worth of inverters, allowing for a total of ~110 MK’s to be built by EOY
It is necessary to target a solution first for the Sprinter platform as we must build on Sprinters until receiving Transits in ~March 2022

## Slide 5: Mitigation Plan
Find replacement for Bel inverter
  Requirement's sheet created
  List of inverters researched in the past has been shared (linked here)
  Replacements are scarce, and will also require SW work to integrate into our control
Utilize an AC generator (like the 1.3), bypassing the need for inverters
  Can prototype with available PowerTech PTI-30 30kW diesel generator in stock in Lawton (8 in stock)
    Powertech getting back to us with availability of 25kW and 30kW diesel generators
  Mount in rear battery compartment

## Slide 6: 1.4+AC Generator next steps
Identify generator options
  First choice would be the PowerTech PTI-30 (linked here) as we have inventory for prototyping in house, and we are familiar with this unit from the 1.3
    (8) in stock in Lawton
    Additional quantities available in February (Patrick to confirm numbers)
    Preferable to find a gas replacement for use on Transit
  Complete survey for additional generators
    Requirements
      25kW+ output range with 120VAC/240VAC output
      Weight <1,250 lbs
      Prefer Diesel for Sprinter, gas for Transit
        Gas may be a challenge due to a DOT regulation on gas fuel flow

## Slide 7: 1.4+AC Generator next steps
Solidify requirements
  Do we need shore power transfer switch for refrigeration, heat, and charging aux battery? Yes.
  Do we want to build in 1.4 charging capability? We could put (3) 240V, 50A receptacles that would allow (2) MK’s charging at 50A, or up to (4) charging at 30A
    Go w/(2) receptacles per MK
    If we are charging, it would be beneficial to have a larger fuel supply to avoid need for overnight filling
      Not possible for sprinter
  Determine if we can go w/AC refrigeration compressors, evaluate 24VDC converter

## Slide 8: 1.4+AC Generator next steps
Design and Prototype
  Design a prototype consisting of
    Rear mount PTI-30 Generator
      Kick-off 20G assessment w/EASi
      Kick-off acoustic enclosure design
        Take baseline reading on AMY, estimate where we can net out w/improvements
      Run fuel pickup
    Prototype harnesses and changes to load center
      Locate switch on bulkhead
      Evaluate split vs. single load center
    Design in 12V power supply (aux batteries) for 12V needs
    Specify and source a rectifier or swap to AC compressors for refrigeration
    Identify potential locations for garbage

## Slide 9: 1.4+AC Generator next steps
Balance impact on 2.0
  Do we need to shift and incorporate the generator into the launch config of the MK2.0 (Transit)? Yes.
Prototype vehicle
  Consider using IVY for prototype #1 (not production)
  Use production 1.4 for vehicle #2
Schedule a Design Review for Gen variant (Op’s + Legal)
  Noise – Where do we think we will end up
  Trash – What will we loose
  Include Mike D, Logan, Culinary, Legal

## Slide 10: Reference (rear mount gen on 1.3)
Picture on right is of AMY which features the PTI-30 with a rear mount
There is an enclosure to block out sound and fumes to the kitchen
Large vents on curbside and streetside without acoustic treatment

## Slide 11: Reference (1.3 Block Diagram)

## Slide 12: Reference (1.3 Gen to Load Center)